## Slide 1
AME 585
Project 6 - Bellow
Henry Glover
3/02/2025

## Slide 2
#1
Bellows are manufactured expansion joints that require high strength and good flexibility.
  These are elastic vessels that can be compressed when pressure is applied to the outside of the vessel or extended under vacuum
  Allows flexibility and movement of pipe systems
  Used in high pressure systems
Where they are used
  In aerospace
  In chemical plants
  In power systems
  In heat exchangers
  In automotive vehicle parts
  In piping systems
  In petrochemical plants
  In refineries
Other than what is mentioned in the lecture, bellows can be used in the following applications
  On trains or busses, bellows are used to connect or extend a cabin car to another
  Bellows used for air suspension on luxury cars

## Slide 3
#2
Examples of failure
https://ntrs.nasa.gov/api/citations/20050198895/downloads/20050198895.pdf - - Orbiter LH2 Feedline Flowliner Cracking Problem
  Cracks were discovered in the flowlines of the space shuttles liquid hydrogen feedlines
  Nasa detected 3 cracks in the downstream flowliner at the gimble joint in the LH2 feedline at the interface with the low-pressure fuel turbopump
  8 additional cracks were found in other orbiters
  Result of low-stress, high cycle fatigue caused by backflow conditions from the space shuttle main engine
    Caused by the vibratory strains
  A weld repair solution was used to repair all the detachable cracks as well as polishing all slot edges to remove manufacturing discrepancies that could initiate new cracks
https://www.materialsperformance.com/articles/material-selection-design/2021/06/failure-of-expansion-joint-caused-by-corrosion-cracking
  A below expansion joint made of type 304 stainless steel exploded in a methane gas pipeline
  Operating temperature was around 400 Celsius
  Deemed to have been caused by stress corrosion cracking induced by hydrogen sulfide present in the gas stream
  Combined with stainless steel, the hydrogen sulfide led to a corrosive environment
  The corrosive environment led to a crack initiation followed by propagation under the operational stresses of pressure and elevated temperature

## Slide 4
#3
Bellow Type | Pros | Cons
Single Bellow | Simplest type of expansion joint. Can absorb small amounts of axial, lateral, and angular movement. | Needs adequate anchors and guides. Limited movement capabilities
Universal Expansion Joint | Allows large axial, lateral, and angular movement. Consists of two single bellows connected by a center spool piece. | Needs adequate anchors and guides. Requires greater number of external restraints to counteract pressure thrust.
Externally Pressurized Expansion Joint | Good for large axial movements. Have self-draining convolutions. | More expensive, harder to install, complex design.
Tied Single bellows | Has design flexibility, tie rods eliminate the need for main anchors. | Cannot absorb axial growth, still needs a well-planned guide system, only lateral and angular movement can be absorbed.
Tied Universal Expansion Joint | Tie rods absorb pressure thrust and limit lateral deflection | Requires precise alignment, has complex installation
Hinged Expansion Joint | Allows angular movement while absorbing pressure thrust, used in pairs to absorb large amounts of expansion, the hinge hardware can carry the pressure thrust of the system and can be used to combat torsional movement | Movement is limited to angulation in one plane, does not allow axial or lateral movement
Gimbal Expansion Joint | Can absorb pressure thrust and torsional twist while allowing angulation in any plane, when paired, it can absorb movement in multi-planer piping systems | Large system and requires complex design
Metal Bellows | High temperature and pressure resistance, very high strength | Fatigue, prone to cyclical loading failure, can be prone to corrosive environments, expensive
Rubber Bellows | Good vibration, shock, and noise absorption, very flexible and can be used in complex piping systems | Low temperature limit, low strength/pressure resistance, easily degradable
Plastic Bellows | Lightweight, corrosion resistant, low cost, | Low temperature limit, low strength/pressure resistance, low mechanical strength
Welded Bellows | Very precise, high strength, reliable in vacuum | Susceptible to corrosive environments, complex manufacturing, susceptible to manufacturing variability

## Slide 5
#4
Parameters that drive bellow selection
  Operating environment
    For space, in vacuum
    Outside or underground
    Underwater
    For high temperature resistance – use, metal bellows
    Low-Temperature but needs flexibility – use rubber or plastic bellows
    Corrosive or chemical resistance – used stainless steel, rubber, or plastic bellow material
  Pressure ratings
    Internal pressure loads
    Use of externally pressurized bellows for high pressure applications
    If axial thrust needs to be absorbed – Use tied, hinged, or gimbal expansion joints
    If no external restraints are needed – externally pressurized bellows or universals bellows will be considered
  Movement requirements
    Axial (compression and extension)
    Lateral
    Angular
    Torsional requirements
Material parameters
  Material formability requirements
  Corrosion properties
  Low cycle fatigue properties
  Good elongation, good weldability, high strength-to-weight ratio
Installation and space constraints
  Large displacements
  Limit space
Cost
  Cost for maintenance
  Cost for installation
Vibration and noise considerations
Application specific requirements
  For aerospace – alloys such as Inconel or titanium
  For vacuum applications – use welded bellows
  For exhaust system – rubber or metal bellows depending on temperature

## Slide 6
#5
Failure Modes
  Fatigue and fracture failure
    High cycle fatigue crack
    Repeated flexing
    Handling damage
    Reduction in fatigue life
      Surface effects – oxidation and local stress risers
      Elevated temperature operation
      Defective welds
  Corrosion and chemical degradation
    Exposure to humidity, salt, chemicals could cause deterioration
  High temperature failure
    Creep (premature deformation under constant stress, especially at elevated temperatures)
  Manufacturing variability and improper installation
  FOD and abrasion
    Foreign objects can cause a bellow to crack or fail
  A loss of pressure containment
    Burst failure or collapse failure caused by overpressure
    Buckling instability from internal and external pressures
  Flow induced vibrations in bellow sections caused
  Inter-ply rupture
  Stress corrosion cracking
  Handling damage
    Dents, scratches, cracks

## Slide 7
#6
Bellow fatigue life
  Fatigue life for metal bellows is affected by primary and secondary mean stress
  Affected by internal stress
  Affected by micro support effects
  Affected by exceeding pressure capacity
  Affected by handling damage and manufacturing variability
How to improve bellow fatigue life
  Optimize convolution geometry
    Shallow, wider convolutions – reduced local stress concentrations
    Uniform convolution profiles – prevents uneven stress distribution
    Avoid sharp transition regions
  Electropolishing
    Coating that improves surface quality for better fatigue life
  Multi-ply bellows
    Multiple thin layers distribute stress better
    Allows for higher flexibility and longer cycle life
    Thicker ply can improve durability, but there needs to be a balance
      Don’t make it too thick, it can reduce flexibility and increase stress from cyclical loads
  Proper material selection
    Work hardened materials – annealing, shot peening
    Corrosion resistance materials
    Fatigue resistance alloys
  Pre-conditioning – subject bellows to few cycles of operating conditions
    This allows the material properties to stabilize
  Minimizing internal pressure stress
  Proper manufacturing and handling

## Slide 8
#7
Recommended requirements for bellow design
  Deflection limitation
    Duct routing should ensure that each flexible joint handles only one type of deflection (angular, axial, or shear) at a time
  Maximum bellows joint deflection
    The total combined deflections on a bellows joint must not exceed its fatigue life stress limits
  Torsional deflection
    Duct assembly design should avoid or minimize torsional loading on the ducts.
  Sizing
    The duct should maintain the required flow area to meet pressure loss limits while being lightweight yet strong enough to withstand all expected loads
  Control of pressure drop
    Flow direction change
      Flow direction changes, such as bends or branch tap-offs, should be designed to minimize pressure loss
    Flow area change
      Changes in flow area should be designed to minimize system pressure drop
    Flow distribution
      Propellant flow needs to be evenly distributed going in and out
    Flow resistance
      Inner surface of the duct needs to have the least amount of possible resistance for flow
  Components
    Separable Connectors
      Flanged duct joints must remain leak-free under operating conditions
    Structural adequacy
      Structure needs to withstand mechncial and dynamic loads during operation

## Slide 9
#7 Cont.
Recommended requirements for bellow design
  Components
    Cleanability
    Brackets and mounting hardware
      Brackets, bosses, and mounting lugs must withstand service loads without cracking or distorting the duct wall
    Insulation
      Thermal resistivity
        Insulation must effectively prevent heat transfer into lines carrying cryogenic fluids
  Leak tightness
    Vacuum jackets cannot leak beyond acceptable limits
  Hot to cold duct interaction
    Withstand thermal loads without leaking when there is a temperature difference in the connection
  Handling protection devices
    Protect critical surfaces of the duct assembly when shipping or handling
  Materials
    Chemical compatibility
      Selected materials must be compatible with the system fluid and external environment throughout storage and service life
    Hydrogen embrittlement
      Ducting and filter materials must resist the harmful effects of a high-pressure gaseous hydrogen environment
    Weldability
      The line material must have sufficient weldability to allow secure attachment of bellows, end flanges, brackets, and bosses
    Formability
      The line material must be formable enough to allow bending or shaping into required convolutions
    Mechanical properties
      The line material's physical and mechanical properties must meet functional requirements and operating conditions

## Slide 10
#8
Flow Induced Vibrations - https://ntrs.nasa.gov/api/citations/19840014844/downloads/19840014844.pdf
  Occur when fluid flow interact with a structure causing oscillations due to pressure forces
  These oscillations and vibrations can lead to fatigue over time, noise, and performance issues
  Can introduce a liner to keep the fluid away from the convolutes
    Expensive and hard to do
  Causes upstream effects
    Momentum fluctuation
    Bubbles in fluid
    Thermal-hydraulic vibration due to phase change
Figure 20 illustrates the vortex formation and shedding process interacting with fluid motion in the convolutes
  From the free stream flow, as the convolutes vibrate, they pump fluid in and out at a velocity, which can strengthen or weaken the vortices depending on the phase relationship. The interaction on the fluid force depends on the vibration amplitude.

## Slide 11
#8 Cont.
Examples of flow induced vibrations
  Vortex induced vibrations
    Fluid flows around a bluff body, vortices are shed creating fluctuating lift forces
    Resonance can amplify oscillation if phase is matched from shedding frequency and natural frequency of the bluff body
    Ex) High velocity stream of gas in a gas pipeline, as fluid flows past convolutes there is vortex shedding creating alternating pressure forces
  Turbulence induced vibrations
    Irregular fluid motion can cause random fluctuations in pressure
    Can cause the convolutes to have unwanted expansion and contraction
    Ex) Heat exchanger tubes that experience turbulent flow
  Acoustic induced vibrations
    High pressure flow generate sound waves that can cause vibrations in the structure
    Ex) High speed fuel flow to an engine
  Fluidelastic variability
    When structural instability are met with fluid forces there can be an unstable feedback loop creating large amplitude oscillations
    Ex) Multi-bellow system used in series can introduce interaction points where vortices form because of interaction points and structural motions of expansion/contraction
  Pressure pulsation-induced vibrations
    Rapid pressure fluctuations lead to pulsating forces
    Ex) Rocket engine fuel feed lines with flexible bellows where a sudden change in fuel flow can create pressure pulsations (can be caused by starvation or bubbles interrupting fluid flow)

## Slide 12
#9
NASA 8123 - https://ntrs.nasa.gov/api/citations/19780008146/downloads/19780008146.pdf
  The main problems in manufacturing of convoluted bellows have been because of material thinning, proper heat-treatment control, proper welding, and convolution stackoff
  Practice of joining bellows is intricate – use weld fixturing, chill blocks, and automatic welding. Electron-beam welding and diffusion bonding have their advantages for joining dissimilar metals. For heat treatable bellows vs non heat treatable, a transition section is used to attached the two dissimilar bellows.
  Fatigue failures of liners in which cracks appeared in the trailing edge and in the weld joint are common – caused by vibrations .
  When routing, the pressure drop in a convoluted inner core is 10 to 15 times that for a comparable diameter hard tube.
  On most flexible hose designs, it is practice to keep velocities of gases below Mach number of 0.3 to avoid pressure loss and flow induced vibrations
  Interconnecting ducts/bellows are routed based on where the optimal positions are for the rocket engine components, not the other way around.
  The maximum effective line stress is limited to a factor of safety of 1.4 on combined loading and 1.5 on ultimate and 1.1 on yield for pressure loading.
  Flow contraction pressure losses can be reduced by 90% if the edges of the contraction are radiused rather than sharp.
  Surface friction between the duct walls and the flowing fluid can produce large pressure losses if the walls are rough.
  To reduce weight, the number of separable connectors used in the line assembly is kept to a minimum. Need to be easily accessible for maintance as well.

## Slide 13
#10
Design Problem 1
  Requirements
    Needs to be lightweight
    Single bellow with 4 plies
    LOX = -297F to 160F
    P = 1000 Psi
    Axial extension = 0.15 in
    Design cycle = 5000
    Internal diameter = 10 in
    Free length = 10 in
  Choose a corrosive resistance material
  Ensure bellows does not yield
  Lightest material possible
  Approach
    Using the EJMA worksheet
    Material properties from MMPDS (2003)
    Plug material properties into worksheet to see which one is best case
    Thinking about using AL T6 or T8 because of low cycle count (5000)

## Slide 14
#10 Cont.
Thanks to Tony, I only considered Aluminum 2195-T8 and Aluminum 2219-T8
Used the excel worksheet to plug in values to get properties
For Aluminum 2195-T8 (https://www.makeitfrom.com/material-properties/2195-2195-T8-Aluminum)
  Yield strength = 82 e3 Psi
  Yield strength at 160F = 77.9 e3 Psi
  Elastic modulus = 10 e6 Psi
  Density = 0.110 Ib/in3
  Weight = 0.144 Ib

## Slide 15
#10 Cont.
For Aluminum 2219-T8
  Yield strength = 61 e3 Psi
  Yield strength at 160F = 57.95 e3 Psi
  Elastic modulus = 10.5 e6 Psi
  Density = 0.103 Ib/in3
  Weight = 0.165 Ib

## Slide 16
#10 Cont.
Final choice is Aluminum 2195-T8
Properties are listed below
Fatigue life
  5000 cycles is low and is a LCF concern
Resonance check
  Bellow has 3.5 convolutions = 4 inner convolutions
  Natural frequency is 85 Hz
Bellow mass
  Total weight = Dry mass + LOX mass
  Convolutions are idealized as semi-circles with a radius equal to their depth

## Slide 17
#10 Cont.
Hand Calc

## Slide 18
#10 Cont.
Model dimension and setup
  Fillet = 0.25
  Length = 10 in
  4 total convolutions
Load parameters
  Pressure = 1000 Psi
  Top node = encaster (fixed)
  Bottom Node = Displacement/rotation = 0.15

## Slide 19
#10 Cont.
Abaqus Run 1
  Run 1 used a thickness of 0.064in
  Results were way below our allowable had more room to reduce thickness
  Max stress = 1.359e5

## Slide 20
#10 Cont.
Abaqus Run 2
  Run 2 used a thickness of 0.144 in
  Results were still below our allowable had more room to reduce thickness
  Max stress = 6.233e4

## Slide 21
#10 Cont.
Abaqus Run 3
  Run 3 used a thickness of 0.12 in
  Results were still below our allowable had more room to reduce thickness
  Max stress = 6.915e4

## Slide 22
#10 Cont.
Abaqus Run 4
  Run 4 used a thickness of 0.104in
  Results are now right under our allowable and we had no more room to reduce thickness
  Max stress = 7.78e4
  Remember allowable = 7.79e4
  These results are within our boundaries and as close as possible to max allowable

## Slide 23
#10 Cont.
Abaqus Conclusion and Strains
  Run 4 with a thickness of 0.104in was my best result
  Results are now right under our allowable and we had no more room to reduce thickness
  Max stress = 7.78e4
  Remember allowable = 7.79e4
  These results are within our boundaries and as close as possible to max allowable
  Max strain for this run was 5.431e3